DATA SHEET

ZARZIS A710 - DIVING SUPPORT VESSEL

Technical Specifications:

Overall length:	36.62 m

Beam:		8.60 m

Draught:		1.70 m

Maximum speed:	17 knots (32 km/h)

Full load

displacement:	230 tonnes approx

Diving equipment:

1 hyperbaric chamber for 4 divers

1 wet bell for 3 divers

1 LARS (launch and recovery system)

Engines:

2 MTU 12V2000 M84

2 x 1220 Kw @ 2450 rpm

Classification: 		RINA C ✠ Hull 	  Mach – Osv (Diving Support)

Offshore Navigation – Dyna – Pos

Main characteristics:

The Diving Support Vessel is equipped with a sophisticated DP2 dynamic positioning system, which combines the push of the main propulsion propellers with that of the bow thrusters, to ensure that exactly the same position is maintained.

The vessel is equipped with:

- decompression chamber;

- production, purification and storage system for breathable air and therapeutic gas;

- a diving bell which can take students into the water up to 100 metres deep.

The vessel is equipped with a LARS (launch and recovery) system to ensure that the diving bell can be immersed and recovered safely.

The diving bell is a semi-open structure that can hold up to 4 divers. Each diver has an umbilical cable that provides breathable gas supply, audio-video communications and hot water supply to control body temperature. The structure can achieve the considerable operational depth of 100m.

On board is also present a system to produce breathable air and NITROX, a special breathing gas mix with a greater oxygen component than normal air. This gas mix can increase diving times at average depths and reduce contextually the amount of nitrogen present in the air breathed, the main gas responsible for any decompression sickness.